The EasySDK Guide
# Format of EasySDK Cartridges
Cartridges according to this document have to be started with both, /GAME and /EXROM being active (low). Therefore all explanations in this document refer to this configuration.
When a C64 with such an cartridge is started, bank number 0 becomes visible from $8000 to $BFFF. Your start-up code has to be at $8000 (ROM offset 0). The KERNAL will search for some magic bytes at this address and jump to your code if it finds them.
When we talk about an offset, we refer to the offset inside the ROM bank. The term address means the location where the memory gets visible inside the C64 memory map.
This means that the offset 0 corresponds to address $8000, while the offset $2000 is visible at the address $A000 (except in Ultimax mode).
If you cartridge makes use of the EasySDK File System (EasyFS), it contains a directory structure. This structure resides at bank 0 on offset $2000. The directory may be shorter than $2000 bytes, but not longer. This means that the directory will not exceed the first bank. Currently a directory must not contain more than 255 entries (excluding end mark).
An image may also contain one or more normal 8 kByte, 16 kByte or Ultimax submodules. These have to be placed on bank boundaries, because they are not loaded, but banked in and started. This special feature may be useful for something like CRT collections.
This is the ROM (Flash) memory layout of an EasySDK cartridge using EasyFS:

# Format of EasyFS Directory Entries
Field	Type	Comment
Name	16 bytes	File name, 16 characters PETSCII (?), 0-padded
Flags	1 byte	File type and some flags
Bank	1 byte	ROM bank where the file starts, 0..63
Offset	2 bytes	File start offset in this bank 0x0000..0x3FFF, little endian
Size	3 bytes	File size, little endian
Padding	1 byte

The flags field has following structure:

Bit	7	6	5	4	3	2	1	0
Meaning	H	R	R	Type

The bit H means hidden. This file is not intended to be seen by a user, a file browser should not show it.

Following Types are defined:
Value	Type
0x00	Files with this type are marked as invalid, they must be skipped. Note that the flags of this file may be not be 0.
0x01	Normal PRG file with 2 bytes start address
…
0x10	Normal 8 kByte cartridge (0x8000..0x9FFF)
0x11	Normal 16 kByte cartridge (0x8000..0x9FFF, 0xA000..0xBFFF)
0x12	Normal Ultimax cartridge (0x8000..0x9FFF, 0xE000..0xFFFF)
0x13	Normal Ultimax cartridge, first bank not used (0xE000..0xFFFF)

0xFF	End of directory. This entry is only a terminator.

# Writing Start-Up Code
The C64 Kernal provides an auto-start for cartridges. To be started automatically, our cartridge must have some magic bytes at bank 0, offset 0. All in all this header has nine bytes.
The first two bytes are the Cold Start vector, this is where the executions starts after a reset. The next two bytes are the Warm Start vector, this one will be called when the Restore key is pressed. Typically these two vectors point to a location inside the ROM area.

The next 5 magic bytes must have the values $C3, $C2, $CD, $38, $30. The following table shows a typical header:

Offset	0	1	2	3	4	5	6	7	8
Value	09	80	A0	80	C3	C2	CD	38	30
Meaning	Cold Start		Warm Start		'C' + 128	'B' + 128	'M' + 128	'8'	'0'

Our program or data may start at offset 9.

In the directory EasySDK/examples/minimal-crt you can find an ACME source code for a tiny CRT image which shows this construction.

If you write start-up code for an cartridge which makes use of EasyFS, make sure your program fits into the area $8000 to $9FFF, because the directory starts at $A000.